## Slide 1
NEZHA INVENTORS KIT V2
CASE 05
The Kaleidoscope Robot
LESSON
05
GRADES
6–8
PERIODS
3 × 45 min
FRAMEWORK
5E Model
LESSON 05
Design & Build
The Kaleidoscope Robot
Robotics
Art
STEAM
Engineering
Motor Control • Rotational Motion • Pattern Creation • Symmetry • MakeCode
Techtelligence Technologies LLC | In partnership with Elecfreaks

## Slide 2
📋 LESSON OVERVIEW
Subject Area
STEM, Robotics, Computer Science
Grade Level
Grades 6–8 (adaptable for Grades 5 & 9)
Duration
3 Class Periods × 45 Minutes = 135 Minutes Total
Framework
5E Instructional Model (Engage → Explore → Explain → Elaborate → Evaluate)
Key Themes
Motor Control • Rotational Motion • Pattern Creation • Art-Science Integration
Materials
NEZHA Kit V2 • Markers • Large paper • MakeCode IDE • Optional: Projector

## Slide 3
🎯 SMART LEARNING OBJECTIVES
01
DESIGN
Build a robot that creates reproducible kaleidoscopic patterns through motor-controlled marker movement.
02
PROGRAMMING
Write a MakeCode program controlling motor speed, direction, and duration to produce precise pattern sequences.
03
SCIENCE
Explain how motor rotation rate and timing interact to produce patterns with specific geometric properties.
04
ART+MATH
Identify and explain the connections between rotational motion, mathematical symmetry, and artistic pattern design.

## Slide 4
📚 KEY VOCABULARY
Motor
Converts electrical energy into rotational mechanical motion.
Rotation
Circular movement around a central axis or pivot point.
Pattern
A repeated or regular arrangement of shapes, colors, or movements.
Symmetry
Balanced arrangement where one side mirrors or repeats the other.
Algorithm
Step-by-step instructions a computer follows to complete a task.
Iteration
Repeating the design-test-improve cycle to optimize an outcome.
Frequency
How often a repeated motion or event occurs per unit of time.
Amplitude
The magnitude of a motion or oscillation from its center point.

## Slide 5
⚡ LESSON FLOW — 5E MODEL (3 Periods × 45 min)
ENGAGE
Period 1 | 40 min
Show kaleidoscope images & video
Guiding questions: shapes, patterns, symmetry
Challenge: 'Build a robot that draws kaleidoscope patterns!'
EXPLORE
Period 2 | 90 min
Experiment with motors & MakeCode
Attach markers, test on poster board
Collaborate; share pattern observations
EXPLAIN
Period 3a | 40 min
Motor mechanics: electricity → rotation
Programming: speed %, direction, duration
Art-science connection: how math creates art
ELABORATE
Period 3b | 25 min
Design a specific reproducible pattern
Iterate: adjust speed & timing to refine
Extensions: color-switching, layered patterns
EVALUATE
Period 3c | 20 min
Robot Gallery showcase
Group presentations: design + programming logic
Exit ticket: motor diagram + 3 parameters

## Slide 6
📅 PERIOD 1 — ENGAGE (40 min)
0–8 min
Hook
TEACHER
Show kaleidoscope video. Ask: 'What shapes do you see? What could make a robot draw like this?'
STUDENT
Jot 2 observations about patterns in engineering notebook.
8–20 min
Components
TEACHER
Introduce kit components. Demo motor connection and basic MakeCode 'spin' command.
STUDENT
Experiment freely — connect motor, run a test spin, observe.
20–35 min
Marker Test
TEACHER
Guide marker attachment. Students tape marker to robot arm and run it on poster board.
STUDENT
Produce first pattern; sketch output and label motor settings used.
35–40 min
Wrap-Up
TEACHER
Groups share first patterns. Identify settings that produced most interesting results.
STUDENT
Record the motor settings that created their favorite pattern.

## Slide 7
🔧 PERIOD 2 — EXPLORE (45 min)
0–15 min
Multi-Speed
TEACHER
Introduce multi-speed sequences: fast spin → slow spin → direction change.
STUDENT
Build a 3-phase program: fast 2s → slow 3s → reverse 2s. Run and observe.
15–30 min
Design Challenge
TEACHER
Challenge: create a specific pattern (spiral, star, wave) on purpose.
STUDENT
Plan, code, and test targeted pattern. Iterate at least twice.
30–38 min
Gallery Walk
TEACHER
Facilitate 2-min rotations. Post patterns and settings on wall.
STUDENT
View others' patterns; write 1 strength and 1 suggestion per team.
38–45 min
Prep
TEACHER
Debrief gallery walk. Introduce Robot Gallery challenge for Period 3.
STUDENT
Write goal for final pattern: what pattern, what settings.

## Slide 8
💡 PERIOD 3 — EXPLAIN → ELABORATE → EVALUATE
0–15 min
Explain
TEACHER
Mini-lecture: motor speed → rotation rate → mark frequency → pattern density.
STUDENT
Label diagram connecting motor setting to observed pattern.
15–30 min
Final Build
TEACHER
15 min to finalize design for Robot Gallery.
STUDENT
Complete final program; run 2 reproducibility tests.
30–42 min
Gallery
TEACHER
Robot Gallery: each group demonstrates and explains MakeCode program.
STUDENT
Show pattern, read key settings, explain 1 science concept.
42–45 min
Exit Ticket
TEACHER
Exit ticket: motor diagram + label 3 programming parameters.
STUDENT
Complete individually and submit before leaving.

## Slide 9
💻 MAKECODE PROGRAMMING GUIDE
SAMPLE CODE STRUCTURE — Lesson 05
// on start block
basic.forever(function () {
PlanetX_STEAM.motorTurnWithTime(
emergencyStopMode.A, 50, 2000, // 50% speed forward, 2 seconds
motorDirection.CW
)
basic.pause(1000) // pause 1 second
PlanetX_STEAM.motorTurnWithTime(
emergencyStopMode.A, 50, 2000, // 50% speed reverse
motorDirection.CCW
)
})
Start Speed
Begin at 40–50% to observe controlled motion before increasing
Timing
Adjust pause and run duration to match your mechanism's range of motion
Direction
CW = clockwise | CCW = counter-clockwise — swap if robot moves wrong way
Loop
basic.forever() repeats indefinitely — test for at least 5 complete cycles

## Slide 10
📊 ASSESSMENT BREAKDOWN
COMPONENT
WEIGHT
DESCRIPTION
Exit Ticket
20%
Motor diagram with 3 labeled programming parameters (individual)
Pattern Portfolio
25%
Final pattern with annotated settings and 3-sentence science explanation
Robot Gallery
20%
Live demo with clear verbal explanation of motor control logic
Team Collaboration
20%
Peer rubric: contribution, communication, idea-sharing
Engineering Notebook
15%
Sketches, settings logs, observations, and reflection entry
TOTAL: 100% | All rubrics distributed at start of lesson | Portfolios due at end of Period 3

## Slide 11
🌟 DIFFERENTIATION & SCAFFOLDING
SUPPORT
Provide pre-built frame components so focus stays on programming
Offer simplified MakeCode template with key blocks pre-placed
Allow partner support during the build and testing phases
Use visual reference cards for technical vocabulary
CORE
Standard build + code sequence as described in lesson
Complete all data collection and analysis tasks
Present results in 90-second team presentation
Write 3-sentence reflection connecting science to design
EXTENSION
Optimize design parameter by ≥25% beyond core target
Write a formal lab report with hypothesis, data, and conclusion
Research a real-world application of the mechanism studied
Create a tutorial video or guide for younger students

## Slide 12
LESSON 05 COMPLETE
Great Work,
Inventors!
NEZHA INVENTORS KIT V2
Techtelligence Technologies LLC
In partnership with Elecfreaks
✅ Lesson 05 DOCX & PDF available in curriculum folder
📦 Check your engineering notebook for completeness
🔬 Explore the real-world connections section in the DOCX
➡️ Next up: Lesson 06