## Slide 1
NEZHA INVENTORS KIT V2
CASE 07
The Crawling Robot
LESSON
07
GRADES
6–8
PERIODS
3 × 45 min
FRAMEWORK
5E Model
LESSON 07
Design & Build
The Crawling Robot
Robotics
Math
Engineering
Science
Gear Ratios • Motor Control • Crawling Locomotion • Traction • Optimization
Techtelligence Technologies LLC | In partnership with Elecfreaks

## Slide 2
📋 LESSON OVERVIEW
Subject Area
STEM, Robotics, Computer Science, Math
Grade Level
Grades 6–8 (adaptable for Grades 5 & 9)
Duration
3 Class Periods × 45 Minutes = 135 Minutes Total
Framework
5E Instructional Model (Engage → Explore → Explain → Elaborate → Evaluate)
Key Themes
Gear Ratios • Motor Control • Crawling Locomotion • Traction • Optimization
Materials
NEZHA Kit V2 • MakeCode • Whiteboard/Projector • Markers • Rulers

## Slide 3
🎯 SMART LEARNING OBJECTIVES
01
DESIGN
Build a crawling robot using the NEZHA Kit V2 that achieves consistent forward locomotion.
02
MECHANICS
Understand the working principles of electric motors and how gear ratio affects speed and torque.
03
MATH
Calculate gear ratios from data and use quantitative results to make targeted design improvements.
04
ENGINEERING
Explore gear configurations systematically and make data-driven optimizations to improve crawling performance.

## Slide 4
📚 KEY VOCABULARY
Gear Ratio
Ratio of input (driver) teeth to output (driven) teeth; governs speed vs. torque.
Locomotion
The ability of a robot or organism to move from one location to another.
Crawling
Low-to-ground movement using multiple contact points for stability and propulsion.
Optimization
Making systematic adjustments to improve performance toward a goal.
Motor Control
Regulating motor speed, direction, and duration through programming.
Mechanism
An assembly of parts that transmits or transforms motion and force.
Traction
Friction between surfaces allowing a robot's contact points to grip and propel.
Iteration
Repeating the design-test-improve cycle using data from each test.

## Slide 5
⚡ LESSON FLOW — 5E MODEL (3 Periods × 45 min)
ENGAGE
Period 1 | 40 min
Crawling robots & real-world uses: rescue, inspection
Video of crawling robots in action
Class brainstorm: design challenges for crawlers
EXPLORE
Period 2 | 90 min
Build basic crawling robot
Experiment with 3 different gear ratios
Time robot over 50 cm — record data table
EXPLAIN
Period 3a | 40 min
Gear ratio formula and torque-speed trade-off
Which gear configuration gave best results?
Demo programming locomotion in MakeCode
ELABORATE
Period 3b | 25 min
Optimize: choose best gear ratio and refine legs
Add optional sensor for obstacle stopping
Gallery walk: borrow one feature from another team
EVALUATE
Period 3c | 20 min
Group presentations with data table
Q&A: defend your gear ratio choice
Exit ticket: gear ratio problem + optimization sentence

## Slide 6
📅 PERIOD 1 — ENGAGE (40 min)
0–8 min
Hook
TEACHER
Show rescue robot video. Ask: 'What challenges does a crawling robot face that a wheeled robot does not?'
STUDENT
List 3 challenges for crawling vs. wheeled robots in notebooks.
8–20 min
Gear Ratio Demo
TEACHER
Gear ratio demo: turn small gear driving large gear. Measure rotations. Calculate ratio.
STUDENT
Sketch 2 gear configs; calculate and label ratio for each.
20–35 min
Build Frame
TEACHER
Groups begin building crawling frame. Coach structural stability and leg placement.
STUDENT
Assemble base frame; attach legs or contact points per sketch.
35–40 min
Hand Test
TEACHER
First crawl test: push robot by hand to simulate motor. Observe leg motion and stability.
STUDENT
Record: does it crawl? Does it tip? What is the biggest problem?

## Slide 7
🔧 PERIOD 2 — EXPLORE (45 min)
0–15 min
Motor + Code
TEACHER
Guide motor attachment and wiring. Demo MakeCode: motor on → pause → motor off.
STUDENT
Mount motor, wire to Nezha board, download basic program, run first crawl.
15–30 min
Gear Experiment
TEACHER
Gear ratio experiment: try 3 configs; time each over 50 cm.
STUDENT
Record gear ratio, time, and notes for 3 configs in data table.
30–38 min
Optimize
TEACHER
Guided optimization: choose best gear ratio and refine leg design.
STUDENT
Make one gear change and one leg adjustment; run 3 more timed trials.
38–45 min
Gallery Walk
TEACHER
Gallery walk: observe other teams' robots. Note one feature to borrow.
STUDENT
Write 1 strength and 1 improvement suggestion per team.

## Slide 8
💡 PERIOD 3 — EXPLAIN → ELABORATE → EVALUATE
0–15 min
Explain
TEACHER
Mini-lecture: gear ratio formula, torque-speed trade-off graph, traction vs. surface type.
STUDENT
Solve 3 gear ratio problems using real numbers from their data table.
15–30 min
Final Sprint
TEACHER
Final optimization: implement best change identified in gallery walk. 12 min build.
STUDENT
Apply one final mod; run 3 timed trials and calculate average speed (cm/s).
30–42 min
Presentations
TEACHER
Group presentations: show robot, display data table, explain gear ratio choice.
STUDENT
Present 90-sec: initial design → problem → change → result.
42–45 min
Exit Ticket
TEACHER
Exit ticket: gear ratio problem + one sentence about optimization.
STUDENT
Complete individually and submit before leaving.

## Slide 9
💻 MAKECODE PROGRAMMING GUIDE
SAMPLE CODE STRUCTURE — Lesson 07
// on start block
basic.forever(function () {
PlanetX_STEAM.motorTurnWithTime(
emergencyStopMode.A, 50, 2000, // 50% speed forward, 2 seconds
motorDirection.CW
)
basic.pause(1000) // pause 1 second
PlanetX_STEAM.motorTurnWithTime(
emergencyStopMode.A, 50, 2000, // 50% speed reverse
motorDirection.CCW
)
})
Start Speed
Begin at 40–50% to observe controlled motion before increasing
Timing
Adjust pause and run duration to match your mechanism's range of motion
Direction
CW = clockwise | CCW = counter-clockwise — swap if robot moves wrong way
Loop
basic.forever() repeats indefinitely — test for at least 5 complete cycles

## Slide 10
📊 ASSESSMENT BREAKDOWN
COMPONENT
WEIGHT
DESCRIPTION
Exit Ticket
20%
Gear ratio calculation + one-sentence optimization explanation (individual)
Data Table
25%
3+ gear configs tested with times, ratios, and average speed computed
Design Improvement
20%
Justified change with quantitative before/after comparison
Group Presentation
20%
Clear explanation of design rationale, data, and results
Engineering Notebook
15%
Sketches, gear labels, data notes, and reflection
TOTAL: 100% | All rubrics distributed at start of lesson | Portfolios due at end of Period 3

## Slide 11
🌟 DIFFERENTIATION & SCAFFOLDING
SUPPORT
Provide pre-built frame components so focus stays on programming
Offer simplified MakeCode template with key blocks pre-placed
Allow partner support during the build and testing phases
Use visual reference cards for technical vocabulary
CORE
Standard build + code sequence as described in lesson
Complete all data collection and analysis tasks
Present results in 90-second team presentation
Write 3-sentence reflection connecting science to design
EXTENSION
Optimize design parameter by ≥25% beyond core target
Write a formal lab report with hypothesis, data, and conclusion
Research a real-world application of the mechanism studied
Create a tutorial video or guide for younger students

## Slide 12
LESSON 07 COMPLETE
Great Work,
Inventors!
NEZHA INVENTORS KIT V2
Techtelligence Technologies LLC
In partnership with Elecfreaks
✅ Lesson 07 DOCX & PDF available in curriculum folder
📦 Check your engineering notebook for completeness
🔬 Explore the real-world connections section in the DOCX
➡️ Next up: Lesson 08